## Slide 1
Jonn Lantz
Technical Specialist, Electric Propulsion Systems @ Volvo Car Group
Jonn.Lantz@volvocars.com
Using models to Scale agile mechatronics
Case studies at Volvo Car Group
Notes: >>> on behalf of the organizing committee of the 17th International
>>> Conference in Software Product Line Engineering (SPLC), it is my
>>> pleasure to invite you as a keynote speaker. The conference will
>>> take place in Florence, Italy, September 15 - 19, 2014.
>>>
>>> The conference brings together about 200-300 researchers and
>>> practitioners working on methods, techniques, and tools for
>>> efficient and effective development of product lines --- software
>>> and systems that exists in many different variants and configurations.
>>>
>>> We hope that in your talk you could share your experience and
>>> insights on introducing model-based engineering using agile
>>> approaches at Volvo. Agile development offers a fresh perspective in
>>> the context of traditional of software and systems product lines
>>> such as cars, which the SPLC audience will likely appreciate and
>>> find interesting.
>>>
>>> Your keynote would be an exiting and highly motivating experience to
>>> the attendees and especially the students and young researchers
>>> attending the conference. We would be highly honored by your presence.

## Slide 2
About Volvo Car Group
Software
Mechanics
Power
Electronics
Volvo Car Group – Green, safe, premium cars!
Climate change; new legislations (often regional) …
Exponential increase of software in cars…
Modern cars are product lines of complex distributed software in moving, safety critical, (high voltage) volume mechatronics
Quantum
Physicist
-2005
Teacher
-2007
Sw developer & change driver
at Volvo Cars -2013
Technical Expert
Continuous Integration
Research collaboration
About me
Technical Expert in CI, Electric Propulsion Systems
Volvo Cars
A trinity for sustainable automotive business!?
Mechatronics
Automotive mechatronics
Power
engineering

## Slide 3: Software Center
Mission: Improve the software engineering capability of the Nordic Software-Intensive industry with an order of magnitude
Theme: Fast, continuous deployment of customer value
Success: Academic excellence
Success: Industrial impact

## Slide 4
#1 Background. Why are we doing this?
Aim
Activity
Assessment

## Slide 5
The Automotive challenge #1
Working with embedded software? Then you are 20 years behind!?
Why?
A modern premium car can have about 100 ECUs (embedded computers) working in a complicated network
So, the system is not 20 years behind! Can we solve this? What will be required in the (near) future? How fast must we get?

## Slide 6
The Automotive challenge #2
Modern premium cars comes with numerous options
We cannot test vehicles with all possible combinations! There are simply too many…
This includes several hybrid variants – i.e. variants of the mechatronic drive train. Mechanics and software are closely connected.
Consider a product line with 5-10 hybrid/mild hybrid/standard models…
We are not there yet, but almost, and the challenge has to be considered now.
Note also that a car [hardware] is designed to last for ≥10 years. Its like selling volume space probes…

## Slide 7
The Automotive challenge #3
The material cost (still) dominates
If there is a new ECU, CPU, …, which save us a dollar it will be choosen. Hence, we work on unstable platforms and changing Tier1 suppliers.
AUTOSAR is an attempt to create a standardized embedded ECU-system with applications, but the platform independence is still not here yet.

## Slide 8
Massive
parallel
development!
Big bang integration
Approaching scaled mechatronics, the first step
Design (plan)
Integrate in platform
(and system rig test)
Test with vehicle
Local rig-test (HIL)
Loop
back
Distr.
Local design (requirements)
Supplier system dev.
ECU/sw
platf. dev.
Secondary software development; sw dev & integration support (continuous flow)
In-house teams work in parallel, but can meet and discuss.
Short loops are possible.
In-house
Out sourced
In-house
development
Too slow!
Too frustrating!
No innovations! Slow product line dev.
(one by one…)

## Slide 9
Change!
From requirement engineering to in-house (software) development!
Requirements
(wishes, ideas, …)
System design
(architecture attempt)
Detailed requirements
(solution attempt, in word)
Send to supplier
Wait…
Test if it works (as you want).
From requirement engineering (with requirement as core object)
Research
Test vehicle
Virtual
test
(MIL/HIL)
ECU & SW
Supplier (Tier1)
Feedback!
Lost knowledge if supplier is replaced!
Development
… to in-house development,
but still struggling with slow feedback
Executable model
as core object!
Architecture (moderating role)
High level
requirements
MIL, HIL test, integration
Test vehicles
ECU
supplier
Photo: dSpace
... and aiming for Continuous Integration with control models as the core objects for development.

## Slide 10
In-house as solution?
Invest in in-house development!
Key software and hardware are easier to loop and optimize in-house. We gain speed and save money
In-house enables [prepared] scaling and control over variants.
The drawback is increased fixed cost. We cannot design the complete car in-house… Prioritization becomes important.
It takes time to establish the essential (agile) methods. Both competence and mind set has to change.
Ideally we should combine in-house solution with “of the shelf” components… But, reality is unfortunately more complex.

## Slide 11
#2 Modeling
.5

## Slide 12
Using Models to have domain experts as programmers
MDE driver #1: Software modeling (low level, not UML) is a good way to introduce control software development!
Domain experts (mechanics, electronics, power electronics…) are usually not software experts.
Domain Specific [programming] Languages (DSLs), like Simulink, will allow domain experts to develop code.
Simulink (used at VCC) provides an abstraction suitable for not too complicated control systems. Most people used to control algorithms can understand a Simulink model…
H. Burden et. al. 2013

## Slide 13
The modeling abstraction level
There are pitfalls in modelling!
Simulink succeeds (at VCC) since the level is low, close to c, as long as the models are kept small. And, since the models can be executed, with ”almost on target”-properties.
UML has failed* in similar setups since The Model becomes too complicated and difficult to maintain. A model which is not executable will inevitably grow over time. Code generation from a too complicated (meta) model becomes unmanageable.
Graphical languages (popular) works for small models – or you end up in spaghetti.
It is very important that the models can be executed with realistic behavior
Models must be kept small
*See e.g. R. Heldal et. al. 2014 (please ask for more exact ref…)
Abstraction
level
UML, Sys-ML
Simulink
C, C++

## Slide 14
The devil is in the detail
Lower level modelling languages have an advantage: the box can be fully understood.
Development is very much about understanding the system – therefore low level languages succeed.
The box provides abstraction (of the generated code), but it is still easy to understand the function and code it produces. We can also configure the box, without complicating it too much.
This put tough constraints on the abstraction level. It usually cannot be as high as we would like…
.5
/* Product: '<S21>/Product11' */
rtb_TmpSignalConversionAtEngNSafe_EngNSafeOutport2.EngN * .5F;
box
Know your box!

## Slide 15
Model driven engineering (MDE)
MDE driver #2: Test your (sub) system before it exists!
Virtual integration is the art of creating test environments for control software, before the actual components (products, or product lines) are available.
Virtual integration in mechatronics requires Plant models (device models) and Environment models (e.g. a road).
Controller (ECU)
Device
Developers
Supplier(s)
Power supply, Network,…
Software models
Plant Models
Environment models
Note: Plant models are primarily useful where closed loops (controller-device/env.) exists

## Slide 16
#3 Agile. Continuous Integration. Speed.

## Slide 17
Time/readiness
Agile (test driven) process
knowledge
Decisions!
system
component
Agile development
Pay to learn early
Gain knowledge early in projects to avoid workload peaks near deadlines!
V-model
”waterfall” process
Succ.
handovers
Time/readiness
system
knowledge
decision
component
is verified
NOTE: Test and test automation is the key

## Slide 18
Agile development

## Slide 19
Simulink
Learn early by making plant models!
Model Driven Development – Create virtual verification environments!
Although the mechanics, ECU-platform and other mechatronics are not yet delivered, plant models
can be designed – using the best knowledge – and used for early continuous virtual integration.
Some assumptions will be proven faulty, but we learn much faster (compared to not use MDE)
(Ulf Eliasson et. al, presented soon at MODELS 2014)
Knowledge
time
still a knowledge gap,
but much smaller!
modeling,
delivers
knowledge
development based on assumptions
first integration
subsystem control sw
plant model

## Slide 20
Model driven engineering; lessons learned
Controller (ECU)
Device
Domain experts as developers
Supplier(s)
Power supply, Network,…
Realistic functional
test results, early
Realistic system test results, early
2. Platform models
3. Plant &
Environment models
1. System models
Platform
independence?
Approaching Scaled MDE
Best result if we combine Domain expert sw development with efficient Virtual Verification
Automated (fast and easy) integration (model based and real) is essential!
Define modeling domains, build competence and knowledge
Reach platform independent development (e.g. utilizing AUTOSAR)
We usually underestimate the resources needed for testing

## Slide 21
Tutorial: Testing in MDE & mechatronics
Modeling comes with new abbreviations:
MIL = Model in the Loop (that is, test the model itself in a modeled environment). Verify the function (and validate your requirements). Note: At VCC Unit Test is conducted at this level.
SIL = Replace the Model above with its generated code. Verify the same behavior.
HIL = Integrate the generated code in the real ECU, but model everything outside the ECU. Verify that the platform does not interfere with the function.
Note that all three steps above can be automated. Especially the two latter steps are suited for automated regression test – (Virtual) Continuous Integration – locally (sub systems) or with other ECUs and other real devices (box car, system HIL).
Then we can go to the car
.c

## Slide 22
The Model Driven process
Re-invent the classical V-model!
ECU
SYS/MECH
High level
reqs.
CAR test
RIG
HIL
Vehicle
integration
System design tool
(database)
Developed by Tier1 from
requirements
System
ECU
SW Component
MIL
(SIL)
System
MIL
Unit
test
SW
Design
code
gen
Simulink & Simscape
Architecture
Simulink
HIL short loop 24h
Continuous Deployment
short loop
Plant models
ECU integration
SW
MIL-SIL short loop 1h

## Slide 23
… and in real life
ECU
SYS/MECH
SW
High level
reqs.
ECU
integrations
System design tool
(database)
System
ECU
SW Component
SW
Design
Simulink & Simscape
ECU
ready!
Vehicle
ready!
CAR test
Vehicle
integra-
tions
RIG
HIL
(continuous ECU-integration
possible)
Plant models
Assumptions verified
HW Assumptions made

## Slide 24
#4 Languages

## Slide 25
Challenges with agile MDE
SW modeling: Lessons learned:
Some basic agile requirements, as merge, are difficult due to binary or non-textual model file formats.
There are few tools available for testing, automation, CM, etc.
There are no communities for agile modelling
Be prepared to develop your own tools, scripts and CI-environments
Start internal & external communities.

## Slide 26
The important secondary software
Internal services are needed to support development
Model transformations
Integration
Test
CM
Automation: transformations, integrations, test, ...
Secondary software is an enabler to model driven agile embedded development
Non-perfect modeling design, test & CM tools
Young standards (e.g. AUTOSAR) having ”dialects”
Specialized build environments
Lesson learned: keep it in-house! Outsourcing of secondary software seldom works, the required flexibility is too large. Speed is important. Knowledge is important.
(the same conclusion as in requirement engineering; you cannot specify what you don’t know)

## Slide 27
Mixing domains
Can we inspire sw developers and CAE teams (e.g. physical modeling teams) to collaborate closer?
The goal is to understand the (sub-)system
The sw team and the CAE team has to model in a way which enables co-simulation of different domains
… and perhaps even co-work on a common model?
The models shall be used in automated integration and automated MIL/SIL test
Controller (ECU)
Device
Developers
Supplier(s)
Power supply, Network,…
DSL
programming
Plant Models
+
-
Environment models

## Slide 28
Scaling Model design
U0
L
R
Controller
(PWM)
V(t)
If we want to model more of the system – mechanics, electronics, fluid mechanics,…, then a single DSL may not be sufficient
A promising solution is to use different Domain Specific Languages (DSL) specialized for the different domains. Electric Propulsion at VCG has tried out “Simscape” (multi domain modelling, integrated in Simulink) now for 3 years. Other sections are using other languages.
DSLs will allow local organizations to develop faster with better reuse and understanding. The design scales!

## Slide 29
DSL example: modelling mechatronics
Mathematical representation
Control V(t)
U0
L
R
Controller
(PWM)
Graphical representation
V(t)
Model using c-code
…
real MyCircuit_dIdt(t,I,V,R,L,U0) {
return (U0 – V – R*I) / L;
}
/* Use with proper ODE solver */
for(t=0, t =+ dt, t < t_end) {
…
Model representation in Simulink
Model representation in Physical DSL

## Slide 30
Then add one tiny component…
DSL example: modelling mechatronics

## Slide 31
Mathematical representation
Control V(t)
Model representation in Physical DSL
U0
L
R
V(t)
Model representation in Simulink
Rewrite completely > 2x no of blocks
Model using c-code
…
real MyCircuit_dIdt(t,I,V,R,L,U0) {
return (U0 – V – R*I) / L;
}
/* Use with proper ODE solver */
for(t=0, t =+ dt, t < t_end) {
…
Rewrite completely > 2x lines of code
DSL example: modelling mechatronics
U0
L
R
Controller
(PWM)
Graphical representation
V(t)

## Slide 32
A use case: developing dog clutch control software
Auto generated
AUTOSAR ECU model
Test bench
(combined with test tool)
Plant model (Simscape DSL)
Results:
Although the first versions of the clutch model had
numerous faulty assumptions, these where easy to
correct – since the developers now understood the
system! (U. Eliasson et. al. MODELS 2014)
model
reference
library
function developers
CAE developers
test
developers
automated
regression test

## Slide 33
my device
controller
device
The Importance of Testing
Some people believe that a graphical, high level control model, looking sort of like an executable specification, is so descriptive, so simple that no unit test or regression test is required.
Although complexity is hidden from the user in Simulink, it will be revealed in the generated code.
Unit Test, (functional) Regression Test and coverage metrics are absolutely essential!
This is completely wrong
vehicle
integration
test
unit test
functional test
automated
regression test

## Slide 34
Note about testing: use the same language!
We know from experience that developers prefer to conduct testing using the same language as they use for development
Thus, if we develop control code using Simulink at VCC, we should develop test cases using Simulink – or in a tool integrated in Simulink with syntax familiar to Simulink users.
This turns out to be tricky…
Formal verification looks very promising!
But should be integrated in the language used by developers. Why not fully integrate testing in the modeling language?
Test vector design and regression test automation
Tools for traditional testing works well
efficient test suite management, parameter set & test execution
fast simulation (minimize compile time, parallel computing, cloud simulation, …) in normal mode (enabling coverage metrics)
Static analysis
Important, but not facilitated yet! Why not integrate this also? The language should help, not trust, the designer…

## Slide 35
… and in real life
ECU
SYS/MECH
SW
High level
reqs.
ECU
integrations
System design tool
(database)
System
ECU
SW Component
SW
Design
Simulink & Simscape
ECU
ready!
Vehicle
ready!
CAR test
Vehicle
integra-
tions
RIG
HIL
(continuous ECU-integration
possible)
Plant models
Assumptions verified
HW Assumptions made
When available – frequent (continuous) integration on target, with high coverage regression test is essential!
Virtual test is for early learning, real test is for real knowledge! (Thus, HIL must be extended with real mechatronics, real vehicles…)
MDE can be successfully combined with Continuous Integration, but tailor-made tools must be developed (in-house!)

## Slide 36
#5 Scaling agile mechatronics!?

## Slide 37
Organizational aspects
An organization is change; from hardware to mechatronics
New processes and agile ways of working must be developed.
Agile has to be adopted to distributed volume mechatronics
Domain experts must gain competence in programming
SW developers must build up Secondary software …
Mechanical ”waterfall” process
Time/readiness
System design
Requirement eng.
Supplier
Integration test
Vehicle test
Time/readiness
Agile mechatronics process
System design
Requirement eng. (mechanics, platform)
Agile sw team (developers, ECU-tester)
Vehicle test
(Vehicle) Integration test
Supplier
Sec. SW support
(Secondary sw)

## Slide 38
The triple lane supersprint (beta)
An attempt to manage distributed mechatronics development (sub system level)
In-house development on existing platform
Supplier development (ECU & devices)
(In-house) product verification; vehicle test
Time for
one short
loop
Platform update
New functionality (X)
Func. Ready for verification (Y)
New platform &
software
New
functionality
(X)
Verify
functionality
(Y)
supersprint

## Slide 39
Scaling agile mechatronics: agile architecture
At present time agile development (fast looping) over the network is difficult
The CAN network is cheap (we beleave), but not flexible.
Static communication model (periodic signals using a static db) yields full com optimized on a finite bandwidth but also a monolithic architecture -> non-agile
The challenges in modeling (describing, designing, maintaining) the present architecture are considerable -> non-agile
This is an obstacle when scaling agile mechatronics, but not necessarily a complete stopper…
But, yes, the developers would appreciate an open, service oriented, network… However, this has to be studied further.
System detail
Agile!
V-model

## Slide 40
#6 Looking forward

## Slide 41
Looking forward – approaching product based development
The challenge of parallel development Automotive development is usually project based: massive parallel development and big bang integrations. Early system test is difficult, if possible at all.
The result is spikes in the issue management and incomplete testing of the final product
development on multiple parallel sub-systems
(ad hoc reuse from previous project)
Big Bang
integration
Product
(or prototype)
Delivery
Typical issue statistics
with ”integration spikes” and delivery cut off
Project Kick off

## Slide 42
We can never have a full [car] product line ready for Continuous Integration
… but using a virtual product (line) it is possible to get closer. Automation is essential! As is an automated model architecture (Avoid parallel architecture models).
Product driven mechatronics: the virtual product line
Current product
(virtual)
Integrate in platform
(and system rig test)
Test with vehicle
Local rig-test (HIL)
Loop
back
In-house
Out sourced
In-house
development
Reqs, tests.
Short loops
Long loop (but faster!)
Included in long loop
Virtual system test

## Slide 43
Scaling Virtual Integration
subsystem control sw
plant models
subsystem control sw
plant models
subsystem control sw
plant models
subsystem control sw
plant models
…
Full product simulation; complete vehicle MIL
Appealing idea, but comes with considerable challenges:
Multi domain architecture (combine hw and sw architectures.)
Multi domain modeling (integrating electronics, cooling, data, mechanics…)
Multiple DSLs has to be integrated (into one executable model)
Currently working on it…
multi domain bus

## Slide 44
How agile should we be?
Developers, they wanna have fun!
It is great to introduce agile! Get rid of the frustration! Develop and really see that your solution ends up in the vehicle…
This will attract smart developers!
However, if the process is too efficient, too fast we might loose the innovations. Innovations which are done during the normal work…
We want to be an innovation driven company.
… but, we are far from that summit yet.

## Slide 45
Conclusions
Volvo Car Group has successfully combined Model Driven Engineering with methods from Agile Software development.
Use cases demonstrate that MDE is an enabler for Agile in complex mechatronic systems.
Continuous Integration (target builds, regression test) is working well, but suitable tools for testing and test automation in DSL-platforms are still missing.
Physical Modeling (DSL) is useful for readable, reusable and scalable modelling of physical systems, but challenging for large scale MIL testing (due to increased complexity and code generation issues)
We invest a lot in Scaled Virtual Verification – but we are not there yet…
Finally, so why are we 20 years behind in embedded SW development?
No clear answer!
Agile is not generic; it has to be adopted (to mechatronics); adoption takes time.
Unstable platforms; the unit price dominates.
No real open source community for embedded software!?
Higher education is more than 20 years behind!?